Pressure gauges MDA/MDR/MHA/MHR

MDA/MHA				MDR/MHR

Measuring instrument with tube-form spring, for liquid materials pressure measurement, in case they are of low ductility and unable to crystallise.

Produced in accordance with EN 837-1.

The device shall be mounted avoiding shaking, and shall be protected from cold and heat.

Execution:

Body:				50, 63 and 80 mm diameter, ABS plastic.

100 mm diameter, steal with epoxy covering.

Glass				acrylic glass

Connection			Brass MS 58

Measuring body			tube-form spring, copper.

Measuring mechanism		brass, high accuracy

Dial-plate			aluminium, white with black scale

Accuracy			accuracy class 1,6

Maximum temperature		+ 80 оС

1. Dial-Plate

2. Measuring body (tube)

3. Hand

4. Notsched segment

5. Muffle

6. Traction

7. Connection

# Dimensions

| Type | Art.Nr. | Body | Connection C | Measuring limits, bar | A | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | D | B |  |  |  |  |
| MHA 50/4 x ¼” MHA 63/4 x ¼” MHA 63/4 x 3/8” | 03.10.104 03.16.204 03.17.204 | 50 63 63 | 28,5 31 31 | ¼” ax. ¼” ax. 3/8” ax. | 0 – 4 0 – 4 0 – 4 | 48 48 53 | 14 14 14 |
| MHA 80/4 x ¼” | 03.21.104 | 80 | 31 | ¼” ax. | 0 – 4 | 69 | 14 |
| MHR 50/4 x ¼” MHR 63/4 x ¼” MHR 63/4 x 3/8” | 03.12.104 03.18.204 03.19.304 | 50 63 63 | 28,5 31 31 | ¼” rad. ¼” rad. 3/8” rad. | 0 – 4 0 – 4 0 – 4 | 48 48 53 | 14 14 14 |
| MHR 80/4 x ½” | 03.20.204 | 80 | 31 | ½” rad. | 0 – 4 | 69 | 14 |
| MHR 100/4 x ½” | 03.22.204 | 100 | 31 | ½” rad. | 0 – 4 | 83 | 14 |
| MDA 50/6 x ¼” MDA 50/10 x ¼” MDA 50/16 x ¼” | 03.10.106 03.10.110 03.10.116 | 50 50 50 | 28,5 28,5 28,5 | ¼” ax. ¼” ax. ¼” ax. | 0 – 6 0 –10 0 –16 | 48 48 48 | 14 14 14 |
| MDA 63/6 x ¼” MDA 63/10 x ¼” MDA 63/16 x ¼” | 03.16.206 03.16.210 03.16.216 | 63 63 63 | 31 31 31 | ¼” ax. ¼” ax. ¼” ax. | 0 – 6 0 –10 0 –16 | 53 53 53 | 14 14 14 |
| MDA 80/6 x ¼” MDA 80/10 x ¼” MDA 80/16 x ¼” | 03.21.106 03.21.110 03.21.116 | 80 80 80 | 31 31 31 | ¼” ax. ¼” ax. ¼” ax. | 0 – 6 0 –10 0 –16 | 69 69 69 | 14 14 14 |
| MDR 50/6 x ¼” MDR 50/10 x ¼” MDR 50/16 x ¼” | 03.12.106 03.12.110 03.12.116 | 50 50 50 | 28,5 28,5 28,5 | ¼” rad. ¼” rad. ¼” rad. | 0 – 6 0 –10 0 –16 | 48 48 48 | 14 14 14 |
| MDR 63/6 x ¼” MDR 63/10 x ¼” MDR 63/16 x ¼” MDR 63/25 x ¼” | 03.18.206 03.18.210 03.18.216 03.18.225 | 63 63 63 63 | 31 31 31 31 | ¼” rad. ¼” rad. ¼” rad. ¼” rad. | 0 – 6 0 –10 0 –16 0 –25 | 53 53 53 53 | 14 14 14 14 |
| MDR 80/6 x ½ MDR 80/10 x ½” MDR 80/16 x ½” MDR 80/25 x ½” | 03.20.206 03.20.210 03.20.216 03.20.225 | 80 80 80 80 | 31 31 31 31 | ½” rad. ½” rad. ½” rad. ½” rad. | 0 – 6 0 –10 0 –16 0 –25 | 69 69 69 69 | 14 14 14 14 |
| MDR 100/6 x ½” MDR 100/10 x ½” MDR 100/16 x ½” | 03.22.206 03.22.210 03.22.216 | 100 100 100 | 31 31 31 | ½” rad. ½” rad. ½” rad. | 0 – 6 0 –10 0 –16 | 83 83 83 | 14 14 14 |

WATTS Industries Deutschland GmbH

Godramsteiner Hauptstr. 167, D-76829 Landau

Tel 49 6341 9656 – 0, Fax 49 6341 9656 – 560